乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

SPECIFICATION FOR APPROVAL

规   格  说  明   书

CUSTOMER'S CODE

本厂代码:                 FL-PZ-W2021-5-8

DESCRIPTION

品    名:              塑料信号灯metal indicator light

SPECIFICATION

规    格:                 8mm

DATE

编制日期:                2021-05-08

PART NO.

本厂型号:               FL1P-08NW-2

REFERENCE No.

档案编号:              FL-PZ-W2021-5-8-012

| Approved By Customer 编 制 | Qualified By 审 核 | Form Designer 批 准 |
| --- | --- | --- |
| 林安松 | 叶建华 | 林银福 |

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

1图片Picture：

2.图纸drawing：

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

3配件材料component material              4性能参数 performance parameter

| 配件名Component name | 材料material |
| --- | --- |
| 灯罩 lens | PC塑料 PC plastic |
| 灯座 housing | PA66阻燃尼龙 PA66 nylon |
| 螺帽 nut | H59黄铜 H59 nickel plated brass |
| 光源 Light source | LED LED灯 |
| 弹垫 | 钢丝 |
| 导线 Wireway | PVC |
| 项目items | 参数parameter |
| 额定电压 Rated voltage | 3V-780V DC or AC |
| 额定电流 rated current | 20mA |
| 额定功率 rated power | 0.2W |
| 绝缘耐压 Insulation and voltage resistance | 1800V |
| 工作寿命 working life | 100000h |
| 电气寿命 electrical life | 100000次 |
| 耐寒 cold-resistant | -40℃ |
| 耐热 heat-resisting | 80℃ |

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

4. Detailed Picture :

5.LED Specification:

- Emitter 外型图

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

- Absolute Maximum Rating 极限工作参数

| 参数 Parameter | 符号 Symbol | 单位 Unit | 极限参数 Maximum Rating |
| --- | --- | --- | --- |
| 耗散功率 Power Dissipation | P | MW | 60 |
| 连续正向电流 Continuous Forward Current | IF | MA | 25 |
| 反向电压 Reverse Voltage | VR | V | 5 |
| 工作温度范围 Operating Temperature Range | Top | ℃ | -25 to +80 |
| 存放温度范围 Storage Temperature Range | Tst | ℃ | -25 to +90 |
| 最高焊接温度 Soldering Temperature | Tso | ℃ | 260 (for 5 second) |

*Ifp Conditions: Pulse Wide≤10msec≤1/10       瞬间脉冲电流

*Tsol Conditions:3mm from the base of epoxy bulb 最高焊接温度 距胶体3mm

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

- Typical Optical/Electrical Characteristics 光电特性参数

| Color parameters 色参数 |  | Optical Brightness 光亮度 | 0.00 cd/m2 |
| --- | --- | --- | --- |
| Main Wavelength 主波长 | 520.7.0 nm | light intensity 光强度 | 1000 mcd |
| Peak Wavelength 峰值波长 | 632.2 nm | luminous flux 光通量 | 4.8 lm |
| Peak width 峰值带宽 | 21.3 nm | luminous power 光功率 | 0.32 mW |
| colour coordinates xy 色坐标xy | (.1404.7126) | luminous efficacy 发光效率 | 56.81 lm/W |
| colour coordinates u'v' 色坐标u'v' | (.0498.5690) | forward current 正向电流 | 20.00 mA |
| colour purity 色纯度 | 0.758 | alternating voltage 交流电压 | 4.22 V |
| Color temperature 色温 | 8400k | AC power 交流电功率 | 0.084 W |

Notes:

1.Work absolute ratings Ta=25℃ humidity=60% 工作常规值 温度=25℃ 湿度=60%

2.Tolerance of measurement of forward voltage±0.1V  正向电压误差范围±0.1V

3.Test Machine: SSP6612 series LED test system

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

LED LAMP RELIABLITY

●  Test It em s An d Result s

| Type | Test Item | REF. Standard | Test Condition | Note | Number of Damaged |
| --- | --- | --- | --- | --- | --- |
| Environmental Sequence | Temperature Cycle | JIS C 7021 (1997) A-4 | -20℃ →25℃ →80℃ → 25℃ 30m ins ,5m ins ,30mins,5mins | 100 cycles | 0/100 |
|  | High H um idit y Heat Cycle | JIS C 7021 (1997) A-5 | 30℃→ 65℃ 90%R H 24hrs/ 1cycle | 10 cycles | 0/100 |
|  | High Temperature Storage | JIS C 7021 (1997) B-10 | Ta=80℃ | 1000hrs | 0/100 |
|  | Humidity Heat Storage | JIS C 7021 (1997) B -11 | Ta=60℃ RH=90% | 1000hrs | 0/100 |
|  | Low Temperature Storage | JIS C 7021 (1997) B-12 | Ta= -30℃ | 1000hrs | 0/100 |
| Operation Sequence | Life Test | JIS C 7035 (1985) | Ta=25℃ I F= 20mA | 1000hrs | 0/100 |
|  | High Humidity Heat Life Test | * | 60℃ RH=90% I F=20m A | 500hrs | 0/100 |
|  | Low Temperature Life test | * | Ta= -20℃ I F=20m A | 1000hrs | 0/100 |
| Destructive Sequence | Resistance to Soldering Heat | JIS C 7021 (1997) A-11 | Tsol=260 ± 5℃,10sec (3mm from the base of the epoxy bulb) | 1 time | 0/20 |
|  | Solder ability | JIS C 7021 (1997) A-2 | Tsol=235 ± 5℃,5sec (Us ing flux) | 1 tim e (over 95%) | 0/20 |
|  | Lead Pull/Bend Test | JIS C 7021 (1997)A-11 | Load 2.5N (0.25kgf) 0°→ 90°→ 0° Bendi ng 3 tim es | No noticeable dam age | 0/20 |

* Refer to reliability test standard specification for in this line.

| Item | Symbol | T est Condition | Criteria for Judgment |
| --- | --- | --- | --- |
|  |  |  | M in. | M ax. |
| Forward Voltage | VF | IF =20m A | --- | Initial data x 1.1 |
| Reverse Current | IR | VR = 5V | --- | Initial data x 2.0 |
| Luminous Intensity | Iv | IF =20m A | Initial data x 0.7 | --- |

- Criteria for Judging The Damage

乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

6. Resistor Specification ( RMS 1/4W 200kΩ):

- CHARACTERISTI   乐清市裕林电子有限公司

Yueqing Yulin Electronic Co., Ltd

Address：721 huancheng east road tantou liushi yueqing wenzhou    Tel：0577-27878383

website：www.pilotlamp.cn                                   fax：0577-27878383-8027

- CHARACTERISTICS　性 能